Project – 1
https://www.electronicshub.org/water-level-controller-using-8051-microcontroller/
# Water Level Controller using 8051 Microcontroller
Aim - This projects aims to create automate the proccess of controlling the level of water in a tank using a system controlled by a microcontroller.

Description – The system consists of a series of sensors that are used to measure the level of water in the tank. The sensors work on the priciplle of the conductivity of water. The system mentioned in the example consists of 4 wires running up to different levels in the tanks. The circuts will get completed based on the level of water inside the tank. Once the circuits get completed, they produce a signal at the inputs of the microcontroller, which is enabled by the help of transistors.

Based on these signals recieved by the microcontroller, the motors controlling the inlet of water get switched on or off. In addition to these, a 555-timer and a capacitor are connected so as to provide a clock signal to provide a timing signal. The motors get sufficient power to run by the means of a relay system.

Finally, there is an LED display screen connected to the microcontroller that displays the level of water in the tank.

Comments-

While the system is based on a 8051 microcontroller, it can easily be replicated by using an Arduino instead. The system can be improved by increasing the sensitivity by either using more wires or different types of sensors (maybe detecting the level of water by measuringing conductivity and feeding in analog input, instead) .